## Slide 1: Simulations
Single Polorization

## Slide 2: Since Last meeting
Corrected modulation formats
Implement various signal quality measurements
  EVM
  SER
Simulations of SNR as a function OOK power, QAM power, and channel spacing

## Slide 3: Ongoing Simulation
SNR as a function of
  OOK and QAM power: [-10, 6] dBm
  Channel spacing: [30, 200] GHz
Objectives
  Relation between physical layer parameters and SNRs
  Find the range of parameters that allows both channels to work properly

## Slide 4: Ongoing Simulation
OOK+16QAM+OOK

## Slide 5: Ongoing Simulation
OOK channel has less number of symbols, so higher noise?
OOK curve will be less noisy in 1/SNR

## Slide 6: SNR vs #Channels
OOK power = -6 dBm, QAM power = 0 dBm
For both OOK and 16QAM: noise @ 2 OOK channels<=noise @ 40 OOK channels
Again, noisy OOK curves due to insufficient number of symbols

## Slide 7: Signal Quality Measurements
s: constellation point
i: symbol
e: error vector
p: reference vector
or
The corresponding ”SNR” is the inverse of the EVM.
But EVM can reflect the properties of noise better.
The reference vector can be both blind or accurate.
And other measurements, e.g., Q factor, SER, BER, etc.
Ultimately, we should also consider the distribution of error vectors.